|  | 67D SERIES | WIDE INPUT VOLTAGE RANGE |
| --- | --- | --- |
|  |  | 15 WATTS DC-DC CONVERTER |
| FEATURES |  |
| ( 2:1 WIDE INPUT VOLTAGES:9-18V,18-36V,36-72V ( 15 WATTS (2x1x0.4inches) PACKAGE ( EFFICIENCY TO 80% ( P1 INPUT FILTER |  |
| GENERAL SPECIFICATIONS | ELECTRICAL SPECIFICATIONS |
| ( SWITCHING FREQUENCY | : 300KHz TYP. | ( INPUT VOLTAGE RANGE | :12V nominal …9-18V |
| ( OUTPUT RIPPPLE & NOISE | : 100mVp-p(20MHz B.W.) |  | :24V nominal …18-36V |
| ( ISOLATION VOLTAGE | : 1500VDC |  | :48V nominal …36-72V |
| ( ISOLATION RESISTANCE | :109 ohms | ( OUTPUT VOLTAGE ACCURACY | :±2% |
| ( STORAGE TEMPERATURE RANGE | :-40℃ TO 100℃ | ( LINE REGULATION | :±1.0%(HL-LL) |
| ( OPERATING TEMPERATURE RANGE | :-25℃ TO +71℃ | ( LOAD REGULATION(SINGLE) | :±1.0%(100% to 10%) |
| ( SHORT CIRCUIT PROTECTION | : CONTINUOUS | ( LOAD REGULATION(DUAL) | :±2%(100% to 10%) |
| ( CASE MATERIAL | : BLACK COATED COPPER WITH | ( EFFICIENCY | :see table |
|  | NON-CONDUCTIVE BASE | ( EMI/RFI | :six-sided continuous shield |
| PART N0. | INPUT RANGE | OUTPUT VOLTAGE | OUTPUT CURRENT | EFFICIENCY (%) |
| 67D-12S05R | 9-18VDC | 5VDC | 3000mA | 81 |
| 67D-12S12R | 9-18VDC | 12VDC | 1250mA | 83 |
| 67D-12S15R | 9-18VDC | 15VDC | 1000mA | 83 |
| 67D-12D12R | 9-18VDC | ±12VDC | ±625mA | 83 |
| 67D-12D15R | 9-18VDC | ±15VDC | ±500mA | 83 |
| 67D-24S05R | 18-36VDC | 5VDC | 3000mA | 82 |
| 67D-24S12R | 18-36VDC | 12VDC | 1250mA | 84 |
| 67D-24S15R | 18-36VDC | 15VDC | 1000mA | 84 |
| 67D-24D12R | 18-36VDC | ±12VDC | ±625mA | 84 |
| 67D-24D15R | 18-36VDC | ±15VDC | ±500mA | 84 |
| 67D-48S05R | 36-72VDC | 5VDC | 3000mA | 83 |
| 67D-48S12R | 36-72VDC | 12VDC | 1250mA | 84 |
| 67D-48S15R | 36-72VDC | 15VDC | 1000mA | 84 |
| 67D-48D12R | 36-72VDC | ±12VDC | ±625mA | 84 |
| 67D-48D15R | 36-72VDC | ±15VDC | ±500mA | 84 |
| MARKINGS AND DIMENSIONS | PIN CONNECTION |
|  | PIN# | SINGLE | DUAL |
|  | 1 | +VIN | +VIN |
|  | 2 | -VIN | -VIN |
|  | 3 | +VOUT | +VOUT |
|  | 4 | No Pin | Common |
|  | 5 | -VOUT | -VOUT |

# Text boxes

Dimensions:inches/mm

Unless otherwise specified, all tolerances are ±.005/±0.13